Wideband  50 ohm to 200 Transformer

Input	50 ohms		Red and Red

Output	200 ohms	Green and Orange

20 turns trifilar wire wound on Amidon FT50-J core with two windings in series for the 200 ohm winding.

With a 200 resistor across the secondary the primary impedance is measured as follows.

# Frequency		Impedance

5 kHz			26 ohms	55 degrees phase angle

10 			38		36

20			45		20

50			48		7

100			49		3

200			48.5		0

500			48.5		2

5 MHz			52		8

10			54		15

20			61		28

30			65		34

Input impedance with secondary short circuited (leakage reactance)

30 MHz		50 ohms  	85 degrees phase angle.